### TOSHIBA Barcode Printer

#### B-EX4T3 SERIES

# Owner’s Manual

| Safety Summary Personal safety in handling or maintaining the equipment is extremely important. Warnings and Cautions necessary for safe handling are included in this manual. All warnings and cautions contained in this manual should be read and understood before handling or maintaining the equipment. Do not attempt to effect repairs or modifications to this equipment. If a fault occurs that cannot be rectified using the procedures described in this manual, turn off the power, unplug the machine, then contact your authorised TOSHIBA TEC representative for assistance. Meanings of Each Symbol This symbol indicates warning items (including cautions). Specific warning contents are drawn inside the symbol. (The symbol on the left indicates a general caution.) This symbol indicates prohibited actions (prohibited items). Specific prohibited contents are drawn inside or near the symbol. (The symbol on the left indicates “no disassembling”.) This symbol indicates actions which must be performed. Specific instructions are drawn inside or near the  symbol. (The symbol on the left indicates “disconnect the power cord plug from the outlet”.) |
| --- |
| This indicates that there is the risk of death or serious injury if the machines are improperly handled contrary to this indication. |
| Do not use voltages other than the voltage (AC) specified on the rating plate, as this may cause fire or electric shock. | Do not plug in or unplug the power cord plug with wet hands as this may cause electric shock. |
| If the machines share the same outlet with any other electrical appliances that consume large amounts of power, the voltage will fluctuate widely each time these appliances operate. Be sure to provide an exclusive outlet for the machine as this may cause fire or electric shock. | Do not place metal objects or water-filled containers such as flower vases, flower pots or mugs, etc. on top of the machines. If metal objects or spilled liquid enter the machines, this may cause fire or electric shock. |
| Do not insert or drop metal, flammable or other foreign objects into the machines through the ventilation slits, as this may cause fire or electric shock. | Do not scratch, damage or modify the power cords. Also, do not place heavy objects on, pull on, or excessively bend the cords, as this may cause fire or electrical shock. |
| If the machines are dropped or their cabinets damaged, first turn off the power switches and disconnect the power cord plugs from the outlet, and then contact your authorised TOSHIBA TEC representative for assistance. Continued use of the machine in that condition may cause fire or electric shock. | Continued use of the machines in an abnormal condition such as when the machines are producing smoke or strange smells may cause fire or electric shock. In these cases, immediately turn off the power switches and disconnect the power cord plugs from the outlet. Then, contact your authorised TOSHIBA TEC representative for assistance. |

| If foreign objects (metal fragments, water, liquids) enter the machines, first turn off the power switches and disconnect the power cord plugs from the outlet, and then contact your authorised TOSHIBA TEC representative for assistance. Continued use of the machine in that condition may cause fire or electric shock. | When unplugging the power cords, be sure to hold and pull on the plug portion. Pulling on the cord portion may cut or expose the internal wires and cause fire or electric shock. |
| --- | --- |
| Ensure that the equipment is properly grounded. Extension cables should also be grounded. Fire or electric shock could occur on improperly grounded equipment. | Do not remove covers, repair or modify the machine by yourself. You may be injured by high voltage, very hot parts or sharp edges inside the machine. |
| Do not use a spray cleaner containing flammable gas for cleaning this product, as this may cause a fire. | Care must be taken not to injure yourself with the printer paper cutter. |
| This indicates that there is the risk of personal Injury or damage to objects if the machines are improperly handled contrary to this indication. |
| Precautions The following precautions will help to ensure that this machine will continue to function correctly. ( Try to avoid locations that have the following adverse conditions: * Temperatures out of the specification * Direct sunlight * High humidity * Shared power source * Excessive vibration * Dust/Gas ( The cover should be cleaned by wiping with a dry cloth or a cloth slightly dampened with a mild detergent solution. NEVER USE THINNER OR ANY OTHER VOLATILE SOLVENT on the plastic covers. ( USE ONLY TOSHIBA TEC SPECIFIED paper and ribbons. ( DO NOT STORE the paper or ribbons where they might be exposed to direct sunlight, high temperatures, high humidity, dust, or gas. ( Ensure the printer is operated on a level surface. ( Any data stored in the memory of the printer could be lost during a printer fault. ( Try to avoid using this equipment on the same power supply as high voltage equipment or equipment likely to cause mains interference. ( Unplug the machine whenever you are working inside it or cleaning it. ( Keep your work environment static free. ( Do not place heavy objects on top of the machines, as these items may become unbalanced and fall causing injury. ( Do not block the ventilation slits of the machines, as this will cause heat to build up inside the machines and may cause fire. ( Do not lean against the machine. It may fall on you and could cause injury. ( Unplug the machine when it is not used for a long period of time. ( Place the machine on a stable and level surface. |
| Request Regarding Maintenance ( Utilize our maintenance services. After purchasing the machine, contact your authorised TOSHIBA TEC representative for assistance once a year to have the inside of the machine cleaned. Otherwise, dust will build up inside the machines and may cause a fire or a malfunction. Cleaning is particularly effective before humid rainy seasons. ( Our preventive maintenance service performs the periodic checks and other work required to maintain the quality and performance of the machines, preventing accidents beforehand. For details, please consult your authorised TOSHIBA TEC representative for assistance. ( Using insecticides and other chemicals Do not expose the machines to insecticides or other volatile solvents. This will cause the cabinet or other parts to deteriorate or cause the paint to peel. |

TABLE OF CONTENTS

Page

1.	PRODUCT OVERVIEW	E1-6

1.1	Introduction	E1-6

1.2	Features	E1-6

1.3	Unpacking	E1-6

1.4	Accessories 	E1-7

1.5	Appearance	E1-8

1.5.1  Dimensions	E1-8

1.5.2  Front View	E1-8

1.5.3  Rear View	E1-8

1.5.4  Operation Panel	E1-9

1.5.5  Interior	E1-9

1.6	Options	E1-10

2.	PRINTER SETUP	E2-1

2.1	Installation	E2-2

2.2	Connecting the Power Cord	E2-3

2.3	Loading Supplies	E2-4

2.3.1  Loading the Media	E2-5

2.3.2  Loading the Ribbon	E2-13

2.4	Connecting the Cables to Your Printer	E2-15

2.5	Turning the Printer ON/OFF	E2-16

2.6	Key Operations	E2-17

2.7	Online Mode Function	E2-19

2.8	System Mode Function	E2-24

2.9　  Printer Drivers	E2-25

2.10    Print Test	E2-26

3.	MAINTENANCE	E3-1

3.1	Cleaning	E3-1

3.1.1  Print Head/Platen/Sensors	E3-1

3.1.2  Covers and Panels	E3-2

3.1.3  Optional Cutter Module	E3-3

4.	PRINTER SPECIFICATIONS	E4-1

5.	TROUBLE SHOOTING	E5-1

5.1	Error Message	E5-1

5.2	Possible Problems	E5-4

5.3	Removing Jammed Media	E5-5

6.	SUPPLY SPECIFICATIONS	E6-1

6.1	Media	E6-1

6.1.1  Media Type	E6-1

6.1.2  Detection Area of the Transmission Sensor	E6-3

6.1.3  Detection Area of the Reflective Sensor	E6-4

6.1.4  Effective Print Area of Paper	E6-5

6.2	Ribbon	E6-6

6.3	Recommended Media and Ribbon Types	E6-6

6.4	Care/Handling of Media and Ribbon	E6-7

A1	MESSAGES AND LEDS	EA1-1

A2	INTERFACE	EA2-1

A3	PRINT SAMPLES	EA3-1

A4	GLOSSARIES	EA4-1

1.	RODUCT OVERVIEW

  - Introduction

1.2	Features

1.3	Unpacking

Thank you for choosing the TEC B-EX4T3 series bar code printer.  This Owner’s Manual contains from general set-up through to how to confirm the printer operation using a test print, and should be read carefully to help gain maximum performance and life from your printer.  For most queries please refer to this manual and keep it safe for future reference.  Please contact your TOSHIBA TEC representative for further information concerning this manual.

This printer has the following features:

- The print head block can be opened providing smooth loading of media and ribbon.

- Various types of media can be used as the media sensors can be moved from the centre to the left edge of the media.

- Web based functions such as remote maintenance and other advanced network features are available.

- Superior hardware, including the specially developed 23.6 dots/mm (600 dots/inch) thermal print head which will allow very clear print at a printing speed of 2, 3, 4, 5 or 6 inches/sec.

- Besides the optional Cutter Module, there is also an optional Peel off Module, Centronics I/F card, Expansion I/O Card, Narrow width platen kit.

Unpack the printer as per the Unpacking Instructions supplied with the printer.

1.4	Accessories

When unpacking the printer, please make sure all the following accessories are supplied with the printer.

(	Safety precaution	( Head cleaner pen

Quick Installation Manual

(	CDROM

1.5	Appearance

1.5.1	Dimensions

1.5.2	Front View

1.5.3	Rear View

The names of the parts or units introduced in this section are used in the following chapters.

1.5.4	Operation Panel

1.5.5	Interior

Please see Section 3 for further information about the Operation Panel.

  - Options

| Option Name | Type | Description |
| --- | --- | --- |
| Disc cutter module | B-EX204-QM-R | Disc cutter Each time media is cut, the media feed is stopped. |
| Peel off module | B-EX904-H-QM-R | This allows use of on-demand (peel-off) operation or to take-up labels and backing paper together when using the rewind guide plate. |
| Precious Peel off module | B-EX904-HH-QM-R | This allows use of on-demand (peel-off) operation or to take-up labels and backing paper together when using the rewind guide plate. To support peel off minimum 3mm length label. |
| Expansion I/O interface card | B-EX700-IO-QM-R | Installing this card in the printer allows connection to an external device with the exclusive interface. |
| Parallel interface card | B-EX700-CEN-QM-R | Installing this card provides a Centronics interface port. |
| RTC & USB host interface card | B-EX700-RTC-QM-R | This card holds the current time: year, month, day, hour, minute, second and provides a USB host interface. |

2.	PRINTER SETUP

This section outlines the procedures to setup your printer prior to its operation.  The section includes precautions, loading media and ribbon, connecting cables, setting the operating environment of the printer and performing an online print test.

2.1	Installation

To insure the best operating environment and to assure the safety of the operator and equipment, please observe the following precautions.

- Operate the printer on a stable, level surface in a location free from excessive humidity, high temperature, dust, vibration and direct sunlight.

- Keep your work environment static free.  Static discharge can cause damage to delicate internal components.

- Make sure the printer is connected to a clean source of AC power and no other high-voltage devices, that may cause line noise interference, are connected to the same mains.

- Assure that the printer is connected to the AC mains with a three-prong power cable that has the proper ground (earth) connection.

- Do not operate the printer with the cover open.  Be careful not to allow fingers or articles of clothing to get caught in any of the moving parts, especially the optional cutter mechanism.

- Make sure to turn off the power and remove the power cord whenever working inside the printer. For example when changing the ribbon, loading the media, or cleaning the printer.

- For best results, and longer printer life, use only TOSHIBA TEC recommended media and ribbons.

- Store the media and ribbons in accordance with their specifications.

- This printer mechanism contains high-voltage components; therefore you should never remove any of the covers of the machine as you may receive an electrical shock.  Additionally, the printer contains many delicate components that may be damaged if accessed by unauthorized personnel.

- Clean the outside of the printer with a clean, dry cloth or a clean cloth slightly dampened with a mild detergent solution.

- Use caution when cleaning the thermal print head as it will become very hot while printing.  Wait until it has had time to cool before cleaning.  Use only the TOSHIBA TEC recommended print head cleaner to clean the print head.

- Do not turn off the printer power or remove the power plug while the printer is printing or while the ON LINE lamp is flashing.

2.2	Connecting the Power Cord

1.	Make sure that the printer Power Switch is in the OFF (() position.

Connect the Power Cord to the printer as shown in the figure below.

2.	Plug the other end of the Power Cord into a grounded outlet as shown in the figure below.

[Example of US Type]	[Example of EU Type]

2.3	Loading Supplies

2.3.1	Loading the Media

The following procedure shows the steps to properly load the media into the printer so that it feeds straight through the printer.

The printer prints both labels and tags.

1.	Turn off the power and open the Top Cover.

2.	Turn the Head Lever to the FREE position and release the Ribbon Shaft Holder Plate.

3.	Open the Print Head Block.

4.	Turn the Locking Ring counterclockwise and remove the Supply Holder from the Supply Shaft.

5.	Put the media on the Supply Shaft.

6.	Pass the media around the Guide Shaft, then pull the media towards the front of the printer.

2.3.1	Loading the Media (Cont.)

7.	Align the tab of the Supply Holder with the groove in the Supply Shaft, and push the Supply Holder against the media until the media is held firmly in place.  This will centre the media automatically.
Turn the Locking Ring clockwise to secure the Supply Holder.

8.	Place the media between the Media Guides and adjust them to the media width.  Once in the correct position tighten the Locking Screw.

9.	Check that the media’s path through the printer is straight. The media should be centered under the Print Head.

2.3.1	Loading the Media (Cont.)

10.	Lower the Print Head Block.

11.	Once the media is loaded it may be necessary to set the Media Sensors used to detect the start position for label or tag.

Setting the Feed Gap Sensor position

(1)	Manually move the Media Sensor so that the Feed Gap Sensor is positioned at the centre of the labels. (( indicates the position of the Feed Gap Sensor).

Setting the Black Mark Sensor position

(1)	Pull about 500 mm of media out of the front of the printer, turn the media back on itself and feed it under the Print Head past the sensor so that the black mark can be seen from above.

(2)	Manually move the Media Sensor so that the Black Mark Sensor is in line with the centre of the black mark on the media.  (( indicates the position of the Black Mark Sensor).

2.3.1	Loading the Media (Cont.)

12.	Batch mode

In the batch mode, the media is continuously printed and fed until the number of labels/tags specified in the issue command have been printed.

2.3.1	Loading the Media

- When the cutter module is fitted:

WARNING!

The cutter blade is sharp, so care must be taken not to injure yourself when handling the cutter.

When the optional cutter module is fitted, insert the leading edge of the media into the cutter until it comes out the media outlet of the cutter cover. The media is automatically cut.

CAUTION：

1.	Be sure to cut the backing paper of the label. Cutting labels will cause the glue to stick to the cutter, which may affect the cutter quality and shorten the cutter life.

2.	Cutting tag paper whose thickness exceeds the specified value may affect the cutter life.

- When the high-precision peel-off module is fitted:

When the optional peel-off module is fitted, a label is automatically removed from the backing paper at the strip plate as each label is printed.

- Press the peel-off unit release button to open the peel-off unit.

- Remove enough labels from the leading edge of the media to leave 200mm of backing paper free.

- Insert the leading edge of the backing paper under the backing paper feed roller.

- Close the peel-off unit until it clicks.

- Manually move the peel-off sensor so that it is in line with the center of labels coming out of the media outlet. (Basically, align the sensor with the center of the media outlet)

- Set the ribbon shaft holder plate and turn the head lever to LABEL2 position.

- Close the top cover.

- When the peel-off module is fitted:

- Remove enough labels from the leading edge of the media to leave 500mm of backing paper free.

- Pull the backing paper out of the media outlet, then insert the leading edge of the backing paper under the strip plate.

- Wind the backing paper onto the take-up spool and fix it in position with the take-up clip. (Wind the paper counterclockwise around the spool.)

- Rotate the take-up spool counterclockwise a few times to remove any slack in the backing paper.

- Set the selection switch mounted on the rewinder Ass’y to STANDARD PEEL OFF position.

NOTES:

1.	Be sure to set the selection switch to STANDARD/PEEL OFF position.

2.	Fit the take-up clip so that the longer side of the clip is fitted into the shallow groove in the take-up spool.

3.	Insert the take-up clip fully.

4.	Backing paper can be wound directly onto the take-up spool or a paper core fitted on the take-up spool. When winding backing paper directly onto the Take-up spool, detach the spring plate from the take-up spool by removing the screw. Otherwise, it may be difficult to pull out the wound backing paper roll.
Wind the backing paper onto the take-up spool two or three times, then fasten the backing paper with the take-upclip.
When using a paper core, put a core on the take-up spool without removing the sprint plate, and attach the leading edge of the backing paper to the core with adhesive tape. The take-up clip is not necessary.

2.3.2	Loading the Ribbon

There are two types of media available for printing on: thermal transfer and direct thermal (which has a chemically treated surface).  DO NOT LOAD a ribbon when using direct thermal media.

1.	Grasp the tabs on the top and bottom of the Ribbon Stoppers and move them back to the end of the Ribbon Shaft.

2.	Leaving plenty of slack between the ribbon spools, place the ribbon onto the Ribbon Shafts as shown below.

Ribbon path

2.3.2	Loading the Ribbon (Cont.)

3.	Slide the Ribbon Stoppers along the Ribbon Shafts so that the ribbon

will be centred when fitted.

4.	Lower the Print Head Block and set the Ribbon Shaft Holder Plate aligning its holes with the Ribbon Shafts.

5.	Take up any slack in the ribbon.  Wind the leading tape onto the ribbon take-up roll until the ink ribbon can be seen from the front of the printer.

6.	Turn the Head Lever to Label2 position to close the Print Head.

7.	Close the Top Cover.

2.4	Connecting the Cables to Your Printer

The following paragraphs outline how to connect the cables from the printer to your host computer, and will also show how to make cable connections to other devices.  Depending on the application software you use to print labels, there are 4 ways to connect the printer to your host computer.  These are:

(	An Ethernet connection using the printer’s standard LAN connector.

(	A USB cable connection between the printer’s standard USB connector and your host computer’s USB port. (Conforming to USB 2.0)

(	A serial cable connection between the printer’s  RS-232 serial connector and one of your host computer’s COM ports.

(	A parallel cable connection between the printer’s optional parallel connector and your host computer’s parallel port (LPT).

For details, refer to APPENDIX 2.

2.5	Turning the Printer ON/OFF

2.5.1	Turning ON the Printer

2.5.2	Turning OFF the Printer

When the printer is connected to your host computer it is good practice to turn the printer ON before turning on your host computer and turn OFF your host computer before turning off the printer.

1.	To turn ON the printer power, press the Power Switch as shown in the diagram below.  Note that ( | ) is the power ON side of the switch.

2.	Check that the ON LINE message appears in the LCD Message Display and that the ON LINE and POWER LED lights are illuminated.

1.	Before turning off the printer Power Switch verify that the ON LINE message appears in the LCD Message Display and that the ON LINE LED light is on and is not flashing.

2.	To turn OFF the printer power press the Power Switch as shown in the diagram below.  Note that (() is the power OFF side of the switch.

3.	MAINTENANCE

3.1	Cleaning

3.1.1	Print Head/Platen/Sensors

CAUTION!

1.	Do not use any volatile solvent including thinner and benzene, as this may cause discoloration to the cover, print failure, or breakdown of the printer.

2.	Do not touch the Print Head Element with bare hands, as static may damage the Print Head.

This chapter describes how to perform routine maintenance.

To ensure the continuous high quality operation of the printer, you should perform a regular maintenance routine.  For high usage it should be done on a daily basis.  For low usage it should be done on a weekly basis.

To maintain the printer performance and print quality, please clean the printer regularly, or whenever the media or ribbon is replaced.

1.	Turn off the power and unplug the printer.

2.	Open the Top Cover.

3.	Turn the Head Lever to the “FREE” position, and then release the Ribbon Shaft Holder Plate.

4.	Open the Print Head Block.

5.	Remove the ribbon and media.

CAUTION!

When cleaning the print head, be careful not to damage the print head with hard objects like watches or rings.

3.1.1	Print Head/Platen/	Sensors (Cont.)

3.1.2	Covers and Panels

6.	Clean the Print Head Element with a Print Head Cleaner or a cotton swab or soft cloth slightly moistened with alcohol.

7.	Wipe the Platen, Feed Roller, and Pinch Roller with a soft cloth slightly moistened with alcohol.  Remove dust or foreign substances from the internal parts of the printer.

8.	Wipe the Feed Gap Sensor and Black Mark Sensor with a dry soft cloth.

Wipe the covers and panels with a dry soft cloth or a cloth slightly moistened with a mild detergent solution.

3.1.3	Optional Cutter Module

The disc cutter are available as an option.

1.	Loosen the two Plastic Head Screws to remove the Cutter Cover.

2.	Remove the jammed paper.

3.	Clean the Cutter with a soft cloth slightly moistened with alcohol.

4.	Attach the Cutter Cover.

4.	PRINTER SPECIFICATIONS

This section describes the printer specifications.

| Model Item | B-EX4T3-HS12-QM/CN-R |
| --- | --- |
| Dimension (W x D x H) | 278 mm x 460 mm x 310 mm (10.9” x 18.1” x 12.2”) |
| Weight (kg) | 17 kg |
| Operating temperature range | 5 degC to 40 degC (40 degF to 104 degF) |
| Relative humidity | 25% to 85% RH (no condensation) |
| Power supply | Universal switching power source AC 100 V to 240 V, 50/60 Hz +/- 10% |
| Input voltage | AC100 V to 240 V, 50/60 Hz +/- 10% |
| Power Consumption | During a print job* | 110W |
|  | During stand-by | 15W or less |
|  | During sleep mode | 4.7W |
| Resolution | 600 dpi (23.6 dots/mm) |
| Printing method | Thermal transfer |
| Printing speed | 50.8 mm/sec. (2 inches/sec.) 76.2 mm/sec. (3 inches/sec.) 101.6 mm/sec. (4 inches/sec.) 127.0 mm/sec. (5 inches/sec.) 152.4 mm/sec. (6 inches/sec.) |
| Available media width (including backing paper) | 25.0 mm to 110 mm (0.98 inches to 4.33 inches) |
| Effective print width (max.) | 104.0 mm (4.1 inches) |
| Issue mode | Batch Strip (Strip mode is enabled only when the optional Strip Module is installed.) Cut (Cut mode is enabled only when the optional Cutter Module is installed.) |
| LCD Message display | Graphic type 128 x 64 dots |

*: While 20% slant lines are printed in the specified format.

| Model Item | B-EX4T3-HS12-QM/CN-R |
| --- | --- |
| Bar code types | JAN8, JAN13, EAN8, EAN8+2 digits, EAN8+5 digits, EAN13, EAN13+2 digits, EAN13+5 digits, UPC-E, UPC-E+2 digits, UPC-E+5 digits, UPC-A, UPC-A+2 digits, UPC-A+5 digits, MSI, ITF, NW-7, CODE39, CODE93, CODE128, EAN128, Industrial 2 to 5, Customer Bar Code, POSTNET, KIX CODE, RM4SCC (ROYAL MAIL 4 STATE CUSTOMER CODE), GS1 DataBar |
| Two-dimensional code | Data Matrix, PDF417, QR code, Maxi Code, Micro PDF417, CP Code |
| Font | Times Roman (6 sizes), Helvetica (6 sizes), Presentation (1 size), Letter Gothic (1 size), Prestige Elite (2 sizes), Courier (2 sizes), OCR (2 types), Gothic (1 size), Outline font (4 types), Price font (3 types) 24 x 24 Simp-Chinese font , 16x16､24x24､32x32､48x48 Gothic- Japanese Font |
| Rotations | 0, 90, 180, 270 deg |
| Standard interface | USB interface Serial interface LAN interface |
| Optional interface | Parallel interface (B-EX700-CEN-QM-R) Expansion I/O interface (B-EX700-IO-QM-R) USB host interface (B-EX700-RTC-QM-R) |

5.	SUPPLY SPECIFICATIONS

5.1	Media

Please make sure that the media being used is approved by TOSHIBA TEC.  The warranty does not apply when a problem is caused by using media that is not approved by TOSHIBA TEC.

For information regarding TOSHIBA TEC approved media, please contact a TOSHIBA TEC authorized service representative.

5.1.1	Media Type

Two types of media can be loaded for this thermal transfer and direct thermal printer: label or tag.  The table below shows size and shape of the media available for this printer.

|  |  | B-EX4T3-HS |
| --- | --- | --- |
|  | Batch | Cutter | Peel-off (*1) |
| ① Pitch | Min. | 5mm | 25mm | 5mm |
|  | Max. | 500mm | 500mm | 256mm |
| ② Label Length | Min. | 3mm |
|  | Max. | 498mm | 497mm | 254mm |
| ③ Backing paper Width | Min. | 25mm |
|  | Max. | 110mm |
| ④ Label Width | Min. | 13mm |
|  | Max. | 108mm |
| ⑤ Gap | Min. | 2mm | 3mm | 2mm |
|  | Max. | 20mm |
| ⑥ Black mark length | Min. | 2mm | 3mm | 2mm |
|  | Max. | 20mm |
| ⑦ Effective print Width | Max. | 104mm |
| ⑧ Effective print Length | Min. | 3mm |
|  | Max. | 498mm | 497mm | 254mm |
| ⑨ Print speed up/slow down area | Slow up | 1mm |
|  | Slow down | 1mm |
| Thickness | Min. | 0.13mm |
|  | Max. | 0.17mm |
| Max. outer roll diameter | Φ200mm(Φ180, When using built-in Rewinder) *Φ170, when paper tube inner diameterφ50.8 |
| Roll-up method | Inner ・Outer |
| Paper core | ID φ76.2±0.3mm |

(*1) When using the High precision peel-off module（B-EX904-HH-QM-R）.

5.1.2	Detection Area of the Transmissive Sensor

The Transmissive Sensor is movable from the centre to the left edge of media.

The Transmissive Sensor detects a gap between labels, as illustrated below.

5.1.3	Detection Area of the Reflective Sensor

1.   The sensor is movable in the range from the center of the paper to the left end.

2.   The reflectance of the black mark must be 10% or less with a waveform length of 950 nm.

3.   The sensor detects at the center of the black mark.

4.   The black marks, if necessary, must be printed on the labels in the gap areas.

5.   Rectangular holes can substitute the black marks, on the condition that nothing is printed on the back side.	Round holes cannot be detected by the reflective sensor.

Min. 2.0 mm

Reflective Sensor position

Reflective

Sensor

(Center of paper)

Perspective on the back side

View from the print surface

Paper feed direction

Min. 12 mm

6mm	Reflective sensor is movable within this range.

5.1.4  EFFECTIVE PRINT AREA OF PAPER

5.1.4.1	Relationship between Print Head Effective Print Width and Paper Width

Paper position (Left)

Paper position (Right)

Printing area

Outside printing area

3 mm

104mm

3mm

Outside printing area

Feed direction

110.0mm

(Max. paper width)

5.1.4.2   Effective Print Area of Tags and Labels

Detection area

0.6 mm(*4)

0.8 mm from left edge of paper

0.8 mm from right edge of paper

Guaranteed printing area

10 mm to 1500 mm

Label/tag length (Top paper width)

Detection area

0.5 mm(*4)

Feed direction

NOTES:

1.	Print quality in the shaded area is not guaranteed. For the label, printing in the 1-mm width area around the label is not guaranteed as well as the shaded area shown above.

2.	The center of the paper (label and tag) is almost aligned with the center of the print head.

3.	If printing is performed in the shaded area, the ribbon may wrinkle. This may affect the print quality of the guaranteed printing area.

4.	0.8mm when print speed 2ips at continuous and peel-off, 1.2mm when print speed is 3ips~6ips.
1.0mm when print speed 2ips at cut, 1.6mm when print speed is 3ips~6ips.

5.2	Ribbon

Please make sure that the ribbon being used is approved by TOSHIBA TEC.  The warranty does not apply to any problem caused by using non-approved ribbons.

For information regarding TOSHIBA TEC approved ribbon, please contact a TOSHIBA TEC service representative.

|  | B-EX4T3-HS |
| --- | --- |
| Ribbon Width | 40mm to 115mm |
| Max Ribbon Length | 300m. |
| Max Ribbon OD | Φ70mm |
| Ribbon Core | Φ25.7 ±0.3mm |
| Type | Flat head |
| Ribbon winding | Outside |

The table below shows the correlation between ribbon width and media width (backing paper is not included.)

| Ribbon width | Media width |
| --- | --- |
| 60 mm | 25 - 55 mm |
| 90 mm | 56 – 85 mm |
| 110 mm | 86 – 105 mm |
| 115 mm | 106 – 110 mm |

5.3	Recommended Media and Ribbon Types

| Media type | Description |
| --- | --- |
| Vellum paper and labels | General use for low cost applications. |
| Coated paper | Matt coated paper General use including applications that require small letters and/or symbols. Glossy coated paper Used where a high-grade finish is required |
| Plastic films | Synthetic film (Polypropylene, etc.) This water-proof and solvent-resistant material has high physical strength and low-temperature resistance, but poor heat resistance (dependant upon material). This material can be used for labels stuck to recyclable containers, so it can be recycled in the same process. PET film This water-proof and solvent-resistant material has high physical strength, and low-temperature resistance as well as heat resistance. This material is used for many applications, especially where high durability is required. Mode/serial plate labels, caution labels, etc. Polyimide This material gives the best performance on heat resistance (greater than PET film). It is often used for PCB labels as it can withstand passage through a solder bath. |

5.3	Media and Ribbon Types (Cont.)

| Ribbon type | Description |
| --- | --- |
| Smear-less ribbon (Wax resin ribbon) | Good match for coated paper. The printed image will resist water and light rubbing. |
| Scratch and solvent resistance ribbon | Very good match for plastic films (synthetic paper, PET, polyimide, etc.) Scratch and solvent resistance Heat resistance with PET and polyimide. |

Combination of Media and Ribbon

| Media type Ribbon type | Vellum paper and label | Coated paper | Plastic films |
| --- | --- | --- | --- |
| Smear-less ribbon (wax-resin ribbon) |  | ( |  |
| Scratch/solvent resistance ribbon |  |  | ( |

(: Good match

5

5.4	Care/Handling of Media and Ribbon

(	Do not store the media or ribbon for longer than the manufacturer’s recommended shelf life.

(	Store media rolls on the flat end.  Do not store them on the curved sides as this might flatten that side causing erratic media advance and poor print quality.

(	Store the media in plastic bags and always reseal after opening.  Unprotected media can get dirty and the extra abrasion from the dust and dirt particles will shorten the print head life.

(	Store the media and ribbon in a cool, dry place.  Avoid areas where they would be exposed to direct sunlight, high temperature, high humidity, dust or gas.

(	The thermal paper used for direct thermal printing must not have specifications which exceed Na+ 800 ppm, K+ 250 ppm and Cl- 500 ppm.

(	Some ink used on pre-printed media may contain ingredients which shorten the print head’s product life.  Do not use labels pre-printed with ink which contain hard substances such as carbonic calcium (CaCO3) and kaolin (Al2O3, 2SiO2, 2H2O).

For further information, please contact your local distributor or your media and ribbon manufacturers.

# Text boxes

# CE Compliance (for EU only)

This product complies with the requirements of EMC and Low Voltage Directives including their amendments.

Changes or modifications not expressly approved by manufacturer for compliance could void the

user’s authority to operate the equipment.

This equipment has been tested and found to comply with the limits for a Class A digital device,

pursuant to Part 15 of the FCC Rules. These limits are designed to provide reasonable rotection

against harmful interference when the equipment is operated in a commercial environment. This

equipment generates, uses, and can radiate radio frequency energy and, if not installed and  sed in accordance with the instruction manual, may cause harmful interference to radio communications.  Operations of this equipment in a residential area is likely to cause harmful interference in which case the user will be required to correct the interference at his own expense.

(for USA only)

“This Class A digital apparatus meets all requirements of the Canadian Interference-Causing

Equipment Regulations.”

“Cet appareil numérique de la classe A respecte toutes les exigences du Règlement sur le matériel brouilleur du Canada.”

(for CANADA only)

### IP20

Centronics is a registered trademark of Centronics Data Computer Corp.

Microsoft is a registered trademark of Microsoft Corporation.

Windows is a trademark of Microsoft Corporation.

VORSICHT:

- Schallemission: unter 70dB (A) nach DIN 45635 (oder ISO 7779)

- Die für das Gerät Vorgesehene Steckdose muß in der Nähe des Gerätes und leicht zugänglich sein.

Copyright © 2006

by TOSHIBA TEC CORPORATION

All Rights Reserved

570 Ohito, Izunokuni-shi, Shizuoka-ken, JAPAN

Waste Recycling information for users:

Following information is only for EU-member states:

The use of the crossed-out wheeled bin symbol indicates that this product

may not be treated as general household waste.

By ensuring this product is disposed of correctly you will help prevent 
potential negative consequences for the environment and human health, which could otherwise be caused by inappropriate waste handling of this product. For more detailed information about the take-back and recycling of this product, please contact your supplier where you purchased the product.

WARNING

Any other than the specified AC voltage is prohibited.

Prohibited

Prohibited

Prohibited

Prohibited

Prohibited

Disconnect the plug.

Disconnect the plug.

Disconnect the plug.

Disconnect the plug.

Connect a grounding wire.

No disassembling.

Prohibited

Prohibited

CAUTION

NOTES:

1.	Check for damage or scratches on the printer.  However, please note that TOSHIBA TEC shall have no liability for any damage of any kind sustained during transportation of the product.

2.	Keep the cartons and internal packing for future transportation of the printer.

NOTES:

1.	Check for damage or scratches on the printer.  However, please note that TOSHIBA TEC shall have no liability for any damage of any kind sustained during transportation of the product.

2.	Keep the cartons and pads for future transportation of the printer.

NOTES:

1.	Check for damage or scratches on the printer.  However, please note that TOSHIBA TEC shall have no liability for any damage of any kind sustained during transportation of the product.

2.	Keep the cartons and pads for future transportation of the printer.

NOTES:

1.	Check for damage or scratches on the printer.  However, please note that TOSHIBA TEC shall have no liability for any damage of any kind sustained during transportation of the product.

2.	Keep the cartons and pads for future transportation of the printer.

NOTES:

1.	Check for damage or scratches on the printer.  However, please note that TOSHIBA TEC shall have no liability for any damage of any kind sustained during transportation of the product.

2.	Keep the cartons and pads for future transportation of the printer.

NOTES:

1.	Check for damage or scratches on the printer.  However, please note that TOSHIBA TEC shall have no liability for any damage of any kind sustained during transportation of the product.

2.	Keep the cartons and pads for future transportation of the printer.

NOTES:

1.	Check for damage or scratches on the printer.  However, please note that TOSHIBA TEC shall have no liability for any damage of any kind sustained during transportation of the product.

2.	Keep the cartons and pads for future transportation of the printer.

NOTES:

1.	Check for damage or scratches on the printer.  However, please note that TOSHIBA TEC shall have no liability for any damage of any kind sustained during transportation of the product.

2.	Keep the cartons and pads for future transportation of the printer.

NOTES:

1.	Check for damage or scratches on the printer.  However, please note that TOSHIBA TEC shall have no liability for any damage of any kind sustained during transportation of the product.

2.	Keep the cartons and pads for future transportation of the printer.

NOTES:

1.	Check for damage or scratches on the printer.  However, please note that TOSHIBA TEC shall have no liability for any damage of any kind sustained during transportation of the product.

2.	Keep the cartons and pads for future transportation of the printer.

NOTES:

1.	Check for damage or scratches on the printer.  However, please note that TOSHIBA TEC shall have no liability for any damage of any kind sustained during transportation of the product.

2.	Keep the cartons and pads for future transportation of the printer.

NOTES:

1.	Check for damage or scratches on the printer.  However, please note that TOSHIBA TEC shall have no liability for any damage of any kind sustained during transportation of the product.

2.	Keep the cartons and pads for future transportation of the printer.

NOTES:

1.	Check for damage or scratches on the printer.  However, please note that TOSHIBA TEC shall have no liability for any damage of any kind sustained during transportation of the product.

2.	Keep the cartons and pads for future transportation of the printer.

NOTES:

1.	Check for damage or scratches on the printer.  However, please note that TOSHIBA TEC shall have no liability for any damage of any kind sustained during transportation of the product.

2.	Keep the cartons and pads for future transportation of the printer.

NOTES:

1.	Check for damage or scratches on the printer.  However, please note that TOSHIBA TEC shall have no liability for any damage of any kind sustained during transportation of the product.

2.	Keep the cartons and pads for future transportation of the printer.

NOTES:

1.	Check for damage or scratches on the printer.  However, please note that TOSHIBA TEC shall have no liability for any damage of any kind sustained during transportation of the product.

2.	Keep the cartons and pads for future transportation of the printer.

LCD Message Display

Operation Panel

Power switch

Media Outlet

Serial Port

USB Port

Parallel Port (Option)

LAN Port

USB Host Port

（Option）

Expansion I/O (Option)

Power inlet

460 (18.1)

460 (18.1)

460 (18.1)

460 (18.1)

460 (18.1)

460 (18.1)

460 (18.1)

460 (18.1)

460 (18.1)

460 (18.1)

460 (18.1)

460 (18.1)

460 (18.1)

460 (18.1)

460 (18.1)

460 (18.1)

278 (10.9)

291 (11.5)

291 (11.5)

291 (11.5)

291 (11.5)

291 (11.5)

291 (11.5)

291 (11.5)

291 (11.5)

291 (11.5)

291 (11.5)

291 (11.5)

291 (11.5)

291 (11.5)

291 (11.5)

291 (11.5)

310 (12.2)

308 (12.1)

308 (12.1)

308 (12.1)

308 (12.1)

308 (12.1)

308 (12.1)

308 (12.1)

308 (12.1)

308 (12.1)

308 (12.1)

308 (12.1)

308 (12.1)

308 (12.1)

308 (12.1)

308 (12.1)

Dimensions in mm (inches)

Dimensions in mm (inches)

Dimensions in mm (inches)

Dimensions in mm (inches)

Dimensions in mm (inches)

Dimensions in mm (inches)

Dimensions in mm (inches)

Dimensions in mm (inches)

Dimensions in mm (inches)

Dimensions in mm (inches)

Dimensions in mm (inches)

Dimensions in mm (inches)

Dimensions in mm (inches)

Dimensions in mm (inches)

Dimensions in mm (inches)

Dimensions in mm (inches)

Top Cover

Supply Window

ONLINE LED

CANCEL

Ribbon Shaft

Supply Shaft

Locking Ring

Supply Holder

Ribbon shaft holder

Head Lever

Ribbon Stopper

Print head

High temp

Warning

LCD

ERROR LED

PAUSE

FEED

MODE

RESTART

UP

LEFT

RIGHT

ENTER

DOWN

Dumper

NOTE:

To purchase the optional kits, please contact the nearest authorised TOSHIBA TEC representative or TOSHIBA TEC Head Quarters.

Setup Flow

Load a label stock or tag stock.

If using thermal transfer media then load the ribbon.

Set the printer parameters in the system mode.

Reference

Procedure

After referring to the Safety Precautions in this manual, install the printer in a safe and stable location.

2.1	Installation

2.3.1	Loading the Media

2.3.2	Loading the Ribbon

2.6	Printer Setting

If necessary, install the printer driver on your host computer.

If the print start position cannot be detected properly when pre-printed label are used, set the threshold automatically.

If the print start position cannot be detected properly even after automatic threshold setting is performed manually set the threshold.

Turn on the printer power.

If necessary, fine adjust the print start position, cut/strip position, print tone, etc.

Installation

Connecting the power cord

Loading the media

Printer setting

Media sensor position alignment

Loading the ribbon

Connecting to a host computer

Print test

Automatic threshold setting

Manual threshold setting

Turning the power ON

Position and Print Tone Fine adjustment

Installing the printer driver

2.5	Turning the Printer

ON/OFF

2.10	Threshold Setting

2.10	Threshold Setting

2.7	Installing the Printer Drivers

2.8	Print Test

2.4	Connecting the Cables to Your Printer

2.3.1	Loading the Media

Make a print test from your operating environment and check the print result.

Connect the printer to a host computer or network.

Adjust the position of feed gap sensor or black mark sensor according to the media being used.

Connect a power cord to the power inlet of the printer, then to an AC outlet.

2.2	Connecting the Power

Cord

2.9　Position and Print Tone

Fine Adjustment

CAUTION!

1.	Make sure that the printer Power Switch is turned to the OFF position (() before connecting the Power Cord to prevent possible electric shock or damage to the printer.

2.	Connect the Power Cord to a supply outlet with a properly grounded (earthed) connection.

Power Cord

Power Switch

Power Plug

Power Inlet

1.	Do not touch any moving parts.  To reduce the risk of fingers, jewellery, clothing, etc., being drawn into the moving parts, be sure to load the media once the printer has stopped moving completely.

2.	The Print Head becomes hot immediately after printing, allow it to cool before loading the media.

3.	To avoid injury, be careful not to trap your fingers while opening or closing the cover.

WARNING!

CAUTION!

1.	Be careful not to touch the Print Head Elements when lifting the Print Head Block.  This may cause missing dots due to static electricity or other print quality problems.

2.	When loading or replacing the media or ribbon, be careful not to damage the print head with hard objects like watches or rings.

Since the print head element can be easily damaged by shock, please treat it carefully and do not hit it with hard objects.

Care must be taken not to allow a metal object like a ring to touch the print head edge.

Care must be taken not to allow the metal or glass part of a watch to touch the print head edge.

NOTES:

1.	When the Head Lever is turned to FREE position, the Print Head can be raised.

2.	To enable printing the Head Lever must be set to the　LABEL2 position.  (This ensures that the Print Head is closed.)

However, proper position may differ depending on media.  So LABEL1 position is reserved.

3.	Do not turn the Locking Ring on the supply holder counter-clockwise too far or it may come off the Supply Holder.

Top Cover

Print Head Block

FREE

LABEL2

LABEL1

Head Lever

Ribbon Shaft Holder Plate

Locking Ring

Supply Shaft

Supply Holder

NOTE:

Do not over-tighten the Locking Ring of the Supply Holder.

Media

Guide Shaft

Tab

Guide Shaft

Supply Holder

Locking Ring

Groove

Supply Shaft

In the case of media which is inside wound.

In the case of media which is outside wound.

Supply Holder

Print Head

Media Guide

Locking Screw

Media

Media Guide

NOTE:

Be sure to set the black mark sensor to detect the centre of the black mark, otherwise a paper jam or no paper error may occur.

Label

Feed Gap Sensor (()

Media Sensor

Gap

Black Mark

Black Mark Sensor (()

Media Sensor

Media

Cutter cover

Media

Media outlet

Pee-off unit

Peel-off unit release button

Backing paper feed roller

Backing paper

Pee-off unit

Backing paper

Peel-off sensor

Ribbon shaft holder plate

Head lever

Top cover

Take-up Spool

Strip Plate

Take-up Clip

Backing Paper

NOTES:

1.	When attaching the ribbon stoppers, make sure that the pinchers face into the printer

2.	Be sure to remove any slack in the ribbon before printing.  Printing with a wrinkled ribbon will reduce the print quality.

3.	The Ribbon Sensor is mounted on the rear of the Print Head Block to detect a ribbon end.  When a ribbon end is detected a “NO RIBBON” message will appear on the display and the ERROR LED will illuminate.

Ribbon Stopper

Ribbon Shaft

Ribbon Shaft

Print Head Block

Ribbon Take-up Roll

Ribbon Shaft Holder Plate

Expansion I/O (Option)

USB Host Port

(Option)

LAN Port

Parallel Port (Option)

USB Port

Serial Port

Power inlet

CAUTION!

Use the power switch to turn the printer On/Off.  Plugging or unplugging the Power Cord to turn the printer On/Off may cause fire, an electric shock, or damage to the printer.

NOTE:

If a message other than ON LINE appears on the display or the ERROR LED lamp is illuminated.

CAUTION!

1.	Do not turn off the printer power while the media is being printed, as this may cause a paper jam or damage to the printer.

2.	Do not turn off the printer power while the ON LINE lamp is blinking as this may cause damage to your computer.

Power Cord

Power Switch

Power Switch

WARNING!

1.	Be sure to disconnect the power cord before performing maintenance.  Failure to do this may cause an electric shock.

2.	To avoid injury, be careful not to pinch your fingers while opening or closing the cover and print head block.

3.	The print head becomes hot immediately after printing.  Allow it to cool before performing any maintenance.

4.	Do not pour water directly onto the printer.

Care must be taken not to allow the metal or glass part of a watch to touch the print head edge.

Care must be taken not to allow a metal object like a ring to touch the print head edge.

NOTE:

Please purchase the Print Head Cleaner from your authorised TOSHIBA TEC service representative.

Thermal Head

CAUTION!

1.	DO NOT POUR WATER directly onto the printer.

2.	DO NOT APPLY cleaner or detergent directly onto any cover or panel.

3.	NEVER USE THINNER OR OTHER VOLATILE SOLVENT on the plastic covers.

4.	DO NOT clean the panel, covers, or the supply window with alcohol as it may cause them to discolour, lose their shape or develop structural weakness.

Platen

Feed Roller

Pinch Roller

Paper sensor

WARNING!

1.	Be sure to turn the power off before cleaning the Cutter Module.

2.  As the cutter blade is sharp, care should be taken not to injure yourself while cleaning.

Plastic Head Screw

Cutter Unit

NOTES:

(	Data MatrixTM is a trademark of International Data Matrix Inc., U.S.

(	PDF417TM is a trademark of Symbol Technologies Inc., US.

(	QR Code is a trademark of DENSO CORPORATION.

(	Maxi Code is a trademark of United Parcel Service of America, Inc., U.S.

Label

Tag paper

Cut position

Cut position

Stop position

Stop

position

Feed Direction

Black Mark 
(on reverse side)

Black Mark 
(on reverse side)

(

(

(

(

(

(

(

(

(

(

(

(

(

(

NOTES:

1. To ensure print quality and print head life use only TOSHIBA TEC specified media.

2.  When the Disc cutter is used, the minimum label length shall be 18.0 mm – (Gap length/2) or longer.

3. The ratio of a label length to a gap length must be a minimum of 3 to 1 (3:1).

4. When using label stock in cut mode, be sure to cut in the gaps. Cutting labels will cause the adhesive to stick to

the cutter, which may affect the cutter performance and shorten the cutter life.

(Min. 3.0mm when the cutter is used)

11mm

NOTE:

Round holes are not acceptable.

(Min. 3.0mm when the cutter is used)

5mm

Label/tag width (Top paper width)

NOTES:

1.	To ensure print quality and print head life use only TOSHIBA TEC specified ribbons.

2.	To avoid ribbon wrinkles use a ribbon that is wider than the media by 5 mm or more.  However, too much difference in width between the two may cause wrinkles.

CAUTION!

Be sure to carefully review and understand the Supply Manual.  Use only media and ribbons that meet specified requirements.  Use of non-specified media and ribbons may shorten the head life and result in problems with bar code readability or print quality.  All media and ribbons should be handled with care to avoid any damage to the media, ribbons or printer.  Read the guidelines in this section carefully.

E

EO1-33114